| Rapporteur Meeting of Question 13/16 | AVD-XXXX |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | STUDY GROUP 16 |
|  | Original: English |
| Question(s): | 13 | 4 November 2008 |
| RAPPORTEUR MEETING DOCUMENT |
| Source: | France Telecom |
| Title: | Proposed modifications to the draft Recommendation H.IPTV-SDC |
| Purpose: | Proposal |

Summary

This contribution proposes some textual modifications to the current draft Recommendation “IPTV  SDC Mechanisms for service discovery up to consumption for IPTV .

# Introduction

The possibility to use TTS (Time-stamped Transport Stream) for content delivery requires signalling in the "Detailed Service offering" metadata.

# Proposed modifications or additions

Section " 10.1	Linear TV discovery record   TS Full SI "

Associated with the element "Portal URL" we should have the format used by the portal. Is it BML, CEA-2014?

After the element " RTP or direct UDP streaming. By default, RTP streaming is assumed.", it is proposed to insert the following element:

      - MPEG-2 TS or Time-stamped MPEG-2 TS. By default, MPEG2 TS streaming is assumed.

# Conclusion

It is proposed that the modifications proposed in this contribution be accepted and H.IPTV-TDES.2 be modified accordingly.

__________________