| Question(s): | Q.21, Q.22 | Meeting, date: | 22 – 26 June 2009 |
| --- | --- | --- | --- |
| Study Group: | 16 | Working Party: | 2 | Intended type of document (R-C-TD): | C |
| Source: | SCAT |
| Title: | Using one ID code for multiple purposes by the IRP in Annex B of H.IRP |
| Contact: | Noboru Koshizuka YRP Ubiquitous Networking Laboratory The University of Tokyo | Tel:+81 3 5437 2270 Fax:+81 3 5437 2271 Email:koshizuka@sakamura-lab.org |
| Contact: | Tetsuo Kamina YRP Ubiquitous Networking Laboratory The University of Tokyo | Tel:+81 3 5437 2270 Fax:+81 3 5437 2271 Email:kamina@sakamura-lab.org |
| Please don’t change the structure of this table, just insert the necessary information. |

# Introduction

At the last SG 16 meeting (27 January – 6 February 2009, Geneva), Q.21/16 and Q.22/16 decided to request for contributions concerning H.IRP, which should support the requirements mentioned in Clause 7.2 of Y.2213, including using one ID code for multiple purposes.  This document is prepared to provide the information about how the IRP (ID resolution protocol) shown in Annex B of H.IRP supports such one-to-many associations between an identifier and associated information instances.

The requirements about one-to-many associations are described in Clause 7.2 of Y.2213 as follows:

- Support of one-to-many associations between an identifier and associated information instances may be provided

- Different associated information for an identifier may be resolved according to usage context of the identifier, for example, who/when/where/why, which is called context dependent forward identifier resolution

# How the IRP in Annex B of H.IRP supports the one-to-many associations

In the IRP in Annex B of H.IRP, each entry of ID resolution information consists of the seven fields described in Table 2.1.

Table 2.1: List of Data Entry Attributes

| Data Entry Attribute | Description |  |
| --- | --- | --- |
| id | ID indicated by the data entry |  |
| idmask | Bitmask which indicates the effective bit of ID |  |
| attribute | Type of the node which the data points | ↑ ID Resolution information ↓ |
| version | Data entry version |  |
| ttl | Cache expiration date of the data entry (seconds) |  |
| datatype | Data display style |  |
| data | Location information corresponding to the resolution request ID |  |

The ID resolution information registered in the entry is mapping information between ID and its content address, typically holding the server address where content is stored.  Each entry includes a field data which indicates the location information corresponding to the ID and a field attribute which indicates the type of the node which the data points.  Since the database table managing each entry does not impose any key constraints, we may insert the identical data value for the identical ID with different attribute value.

ID resolution, on the other hand, is performed by the following procedure.  An ID resolution request consists of the parameters described in Table 2.2.

Table 2.2: Parameters of ID Resolution Request

| Parameter Name | Description |
| --- | --- |
| queryid | Target ID to be resolved |
| querymask | Bitmask which indicates the effective bit of queryid |
| queryattribute | ID resolution information attribute to be acquired |

If both of the following conditions are met, the database search is successful:

• (queryid & querymask & idmask) equals to (id & querymask & idmask)

• queryattribute equals to attribute.

Thus, each ID may be associated with multiple data and one ID may be used for multiple purposes, which can be indicated by the database entry’s field attribute and the query parameter queryattribute.